## Slide 1
Airborne dust identification from space: a new, MSG/SEVIRI-based method for air quality assessment Prof. Valerio Tramutoli
valerio.tramutoli@unibas.it
University of Basilicata, School of Engineering, Potenza, Italy

## Slide 2
Particular matter PM10
SOURCES
ANTHROPOGENIC
NATURAL
IMPACTS
HUMAN HEALTH
…are responsible for 6% of total mortality
CLIMATE
… cause damage to the cardiovascular and respiratory systems
DIRECT
INDIRECT
High PM10 concentrations…
…impact on reflection and absorption of solar and IR radiation in the atmosphere
…can alter cloud features by acting as condensation nuclei

## Slide 3
DIRECTIVE 2008/50/EC OF THE EUROPEAN PARLIAMENT AND OF THE COUNCIL (21/05/2008)
on ambient air quality and cleaner air for Europe
Where the Commission has been informed of an exceedance attributable to natural sources in accordance with paragraph 1, that excedance shall not be considered as an exceedance for the purposes of this Directive.
ANNEX XI - LIMIT VALUES FOR THE PROTECTION OF HUMAN HEALTH
PM10 | Averaging Period | Limit value
 | One day | 50 μg/m3, not to be exceeded more than 35 times a calendar year
Article 20 – CONTRIBUTIONS FROM NATURAL SOURCES*
Paragraph 2
* Article 2 – Paragraph: 15 Contributions from natural sources’ shall mean emissions of pollutants not caused directly or indirectly by human activities, including natural events such as volcanic eruptions, seismic activities, geothermal activities, wild-land fires, high-wind events, sea sprays or the atmospheric re-suspension or transport of natural particles from dry regions
Local authority actions (e.g. traffic restrictions)

## Slide 4: Dust Storm Spectral Signatures
easier to detect over the sea than over land (low contrast)
Highly reflecting
Solar radiation in the VISible
A Saharan Dust storm during
03/03/04 on a SEVIRI image
SAND
STORM
METEO
CLOUDS
SEVIRI RGB
Usually colder than background surfaces
(in the Thermal InfraRed .TIR)
Like to meteorological
clouds !

## Slide 5: Discriminating meteo from dust clouds the Split Window BTD method (e.g. Prata. 1989, Gu et al., 2003; Luo et al., 2003)
T11m - T12m< 0
T11m - T12m> 0
A Saharan Dust storm during 03/03/04 on a SEVIRI image
Kerkmann Jochen (2010)
DT11m-12m< 0
DT11m-12m> 0
Dust  T11m - T12m< 0
Clouds  T11m - T12m> 0

## Slide 6: Main meteorological (high repetition) satellite sensors with split window capabilities
for timely detection of signal variations
Sensor | Spatial Resolution | Temporal Resolution | Satellite | Available since
AVHRR (Global) | 1,1 Km | 6 h | NOAA/ MetOp | 1978
MODIS (Global) | 0,25 – 1 Km | 12 h | EOS | 1999
SEVIRI (Europe & Africa) Global by Geosttionary Constellation | 1 - 3 Km | 15 min. | MSG | 2003

## Slide 7: Space-Time coverage
Meteosat & MSG receiving station at UNIBAS
NOAA & EOS receiving station
at IMAA
one image every
5-15 minutes
Since 1994
since 2000
one image every
3-6 hours

## Slide 8: TRADITIONAL (FIXED THERSHOLD) METHODS FOR DUST-CLOUD DETECTION Split Window BTD method (e.g. Prata. 1989, Gu et al., 2003; Luo et al., 2003) Main issues: false positives
14/05/1995: no dust storm present over the scene
T11m – T12m < 0
Result of a traditional “split-window”-based method
False Positive
Prata (1989)

## Slide 9: TRADITIONAL (FIXED THERSHOLD) METHODS FOR DUST-CLOUD DETECTION Split Window BTD method (e.g. Prata. 1989, Gu et al., 2003; Luo et al., 2003) Main issues: false positives
ftp://toms.gsfc.nasa.gov/pub/omi/images/aerosol/Y2008/
A
B
A
B
SEVIRI 0,6 μm
ΔT (11μm -12μm) < 0
SEVIRI 06/02/2008_h 13 UTC
ΔT (11μm -12μm) <1
SEVIRI 0,6 μm
A
B
(Prata, 1989)
(Luo, 2003)
N°pixel
ΔT(k)
BB
Luo (2003) threshold
Prata (1989) threshold
AA

## Slide 10: TRADITIONAL (FIXED THERSHOLD) METHODS FOR DUST-CLOUD DETECTION Split Window BTD method (e.g. Prata. 1989, Gu et al., 2003; Luo et al., 2003) Main issues: missed detections
B
A
SEVIRI 0,6 μm
ΔT (11μm -12μm) < 0
SEVIRI 02/02/2008_h 06 UTC
(Prata, 1989)
A
B
ΔT(k)
pixel number
Prata (1989) threshold
SAND STORM
MISSED

## Slide 11: What does “anomaly” mean ? TRADITIONAL (FIXED THERSHOLD) METHODS
time or distance
Signal
anomalies ?
Fixed threshold
tests

## Slide 12: What does “anomaly” mean ? lower thresholds increase sensitivity…
time or distance
Signal
anomalies ?
Fixed threshold
tests
but false alarms too !

## Slide 13
time or distance
Signal
anomalies ?
Fixed threshold
tests
but reduce sensitivity too
What does “anomaly” mean ? higher thresholds increase reliability…

## Slide 14: What does “anomaly” mean ?
Time or space
Vref(r)
Signal at the sensor
ns(r)
anomalies ?

## Slide 15
1. Select an historical data-set V(r,t) as homogeneous as possible: same time of the day and period of the year (T-domain) in order to reduce natural/observational noise
X
Y
t
RST (Robust Satellite Technique) (formerly RAT: Robust AVHRR Techniques, V. Tramutoli, 1998, 2005)

## Slide 16
2. Compute the unperturbed reference fields for the observable V(r,t)
VREF (r) and sV(r)
Febr-Nighttime
Febr-Nighttime
1. Select an historical data-set V(r,t) as homogeneous as possible: same time of the day and period of the year (T-domain) in order to reduce natural/observational noise
X
Y
t
RST (Robust Satellite Technique)

## Slide 17
VREF (r) and sV(r)
Febr-Nighttime
Febr-Nighttime
3. Change - Detection at the time t by
A.L.I.C.E.
(Absolutely Llocal Index of Change of the Environment)
1. Select an historical data-set V(r,t) as homogeneous as possible: same time of the day and period of the year (T-domain) in order to reduce natural/observational noise
2. Computing the unperturbed reference fields for the observable V(r,t)
X
Y
t
RST (Robust Satellite Technique)

## Slide 18: 20 years of RST Applications
Floods
Forest fires
Erli
Carpasio
Casanova Lerrone
Voltri
fires
e.g. Fires in Italy, February 2005
Dust storms
Infrastructures
e.g. 18 October 2005 IRAQ
Explosions
Volcanic Eruptions
e.g. Etna eruption Oct 2002
Ash Clouds
e.g. Oil spill in the Mexico Gulf, April 2010
Oil spill
Deepwater Horizon Location
Oil spills
Soil wetness
e.g. Carpathian Basin, April 2000
Moderately wet
Raining Clouds
Weakly wet
Extremely wet
Earthquakes
e.g. 7 September 1999 Athens Earthquake
Thermal anomalies
3 days before EQ
Flooded areas
e.g. Basilicata flood, March 2011
Dust clouds
e.g.Libia 13 May 2004

## Slide 19: Dust Storm Detection by RST
Compared with the background in (normal) clear-sky conditions both meteorological and dust clouds are characterized by:
higher VIS reflectance
SAND
STORM
METEO
CLOUDS
DESERT
BACKland
AVHRR VIS

## Slide 20: Dust Storm Detection by RST
higher VIS reflectance
METEO
CLOUDS
METEO
CLOUDS
Compared with the background in (normal) clear-sky conditions both meteorological and dust clouds are characterized by:
lower brightness temperatures
Notes: 20

## Slide 21: Dust Storm Detection by RST
Compared with the background in (normal) clear-sky conditions both meteorological and dust clouds are characterized by:
T11m - T12m< 0
T11m - T12m> 0
but they can be discriminated
by using the BTD signature DT= T11m - T12m
higher VIS reflectance
lower brightness temperatures
Notes: 21

## Slide 22
&
&
Dust Storm Detection by RST
(RSTDUST Sannazzaro et al., Acta Astronautica93(2014) 64–70)
Detecting Clouds
Discriminating dust-clouds from meteorological clouds

## Slide 23
RSTDUST application to the event of May 2008:
comparison with fixed threshold methods
and
with independent aerosol products (validation)

## Slide 24
Saharan dust event of 18-23 May 2008
During 18-23 May 2008 a massive Saharan dust load coming from Algeria and Tunisia moved towards Europe diffusing over Greece.
On 18 May, Italy and Central Europe were the regions more affected by dust.
From 19 May also the Eastern Europe was involved by dust.
On 20 May the Saharan dust event was more intense over Greece, where it reached a value of dust loading estimated at around 0.75 g/m2 (Amiridis, et al., 2009).

## Slide 25
SEVIRI satellite data
Repeat cycle: 15 min
Spatial resolution (sub-satellite point): 3×3 Km2 (1×1 Km2 HRV)
Spinning Enhanced Visible and InfraRed Imager (SEVIRI) is on board the Meteosat Second Generation (MSG) platform

## Slide 26
Space-time evolution of dust outbreak of 18-23 May 2008 detected by RSTDUST on SEVIRI data
18/05/2008 00:00 GMT
18/05/2008 06:00 GMT
18/05/2008 12:00 GMT
20/05/2008 00:00 GMT
20/05/2008 12:00 GMT
21/05/2008 00:00 GMT
21/05/2008 06:00 GMT
21/05/2008 12:00 GMT
22/05/2008 00:00 GMT
22/05/2008 06:00 GMT
22/05/2008 12:00 GMT
23/05/2008 00:00 GMT
23/05/2008 06:00 GMT
23/05/2008 12:00 GMT
19/05/2008 00:00 GMT
40°
50°
10°
20°
40°
50°
10°
20°
40°
50°
10°
20°
40°
50°
10°
20°
50°
40°
10°
20°
19/05/2008 06:00 GMT
40°
50°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
50°
40°
10°
20°
RST-DUST maps reporting dynamic evolution (at six hours) of dust event which affected Mediterranean basin in May 2008
probability of dust presence in the atmosphere

## Slide 27
EARLINET stations
Comparison with fixed-threshold methods
19/05/2008 06:00 UTC
Gu et al. (2003)
Luo et al. (2003)
RSTDUST
ΔT < -0.5k
T11 μm >290K & T12 μm >290k & ΔT ≤ 1K
probability of dust presence in the atmosphere
POTENZA EARLINET station indicates the presence of dust
OMI Aerosol index indicates the presence of dust

## Slide 28
Comparison with independent satellite-based aerosol products
RSTDUST
Terra-MODIS AOD product
19/05/2008 at 09:15 UTC
http://ladsweb.nascom.nasa.gov/data/search.html
probability of dust presence in the atmosphere
(10 km spatial resolution)

## Slide 29
50°
40°
10°
20°
30°
19/05/2008 at 09:30 UTC
Assessment of RSTDUST products by means of ground-based lidar profiles (EARLINET data)
probability of dust presence in the atmosphere
Sofia: 43.65 N, 23.38 E
Potenza: 40.6 N, 15.72 E
Naples: 40.83 N, 14.18 E

## Slide 30
RST-DUST 22/05/2008 at 11:30 UTC
Assessment of RSTDUST products by means of CALIOP (Cloud-Aerosol Lidar with Orthogonal Polarization) data
http://www-calipso.larc.nasa.gov/products/lidar/browse_images/production/
probability of dust presence in the atmosphere

## Slide 31
Integration of the RSTDUST satellite products and PM10 ground measurements

## Slide 32
Satellite and ground data used
PM10 concentrations from ARPAB (Regional Environment Protection Agency of Basilicata) air quality monitoring ground stations
MSG-SEVIRI

## Slide 33
Bihourly measurement: air monitoring stations in Rossellino, V. Unicef, V. Firenze, Melfi, S. Nicola-Melfi
Daily measurement: air monitoring station in Viggiano
Time series of ARPAB ground PM10 concentrations
May 2006-2012
May 2006 – PM10
May 2007 – PM10
May 2008 – PM10
May 2009 – PM10
May 2010 – PM10
May 2011 – PM10
May 2012 – PM10

## Slide 34
PM10 exceedances (May 2006, May 2008)
Exceedance day | Monitoring station | PM10 concentrations [μg/m3]
23 May 2006 | Rossellino | 51,326
23 May 2006 | V. Unicef | 74,052
24 May 2006 | Rossellino | 63,008
24 May 2006 | V. Unicef | 67,684
19 May 2008 | V. Firenze | 55,516
27 May 2008 | Rossellino | 55,082
*Daily limit 50 μg/m3 (Dir 2008/50/CE)
Regulatory limit (*)

## Slide 35
Quantifying natural contribution in PM10 (EC, 2011)
Methodology for the determination of re-suspended and transported Saharan dust
EC (2011) - COMMISSION STAFF WORKING PAPER establishing guidelines for demonstration and subtraction of exceedances attributable to natural sources under the Directive 2008/50/EC on ambient air quality and cleaner air for Europe
1. Identifying Saharan dust outbreak episodes (EC, 2011, suggests consultation of products such as dust-forecast models)
The use of RSTDUST product instead of forecast maps is expected to increase reliability of dust events detection
Exceedance day | Monitoring station | PM10 concentrations [μg/m3]
23 May 2006 | Rossellino | 51,326
23 May 2006 | V. Unicef | 74,052
24 May 2006 | Rossellino | 63,008
24 May 2006 | V. Unicef | 67,684
19 May 2008 | V. Firenze | 55,516
27 May 2008 | Rossellino | 55,082
19/05/2008
27/05/2008

## Slide 36
Quantifying natural contribution in PM10 (EC, 2011)
Methodology for the determination of re-suspended and transported Saharan dust
1. Identifying Saharan dust outbreak episodes
2. Quantifying Saharan dust outbreak episodes
Identification of the regional background station
Monitoring station in Melfi

## Slide 37
02 May 2008 ore 12 GMT
02 May 2006 ore 06 GMT
Quantifying natural contribution in PM10 (EC, 2011)
Methodology for the determination of re-suspended and transported Saharan dust
Computation of the regional background level:
in each time series of the regional background station, the monthly moving percentile 40 is determined for each day, excluding days with identified African influence.
02 May 2006 ore 12 GMT
Dust events in background station (identified by means of RSTDUST)
1. Identifying Saharan dust outbreak episodes
2. Quantifying Saharan dust outbreak episodes
06 May 2006 ore 06 GMT
07 May 2006 ore 06 GMT
08 May 2006 ore 06 GMT
12 May 2006 ore 12 GMT
25 May 2006 ore 12 GMT
30 May 2006 ore 12 GMT
11 May 2008 ore 06 GMT
19 May 2008 ore 06 GMT
22 May 2008 ore 12 GMT
23 May 2008 ore 12 GMT
26 May 2008 ore 06 GMT
27 May 2008 ore 06 GMT
28 May 2008 ore 12 GMT
29 May 2008 ore 06 GMT

## Slide 38
PM10 anomalies under exceedance limit
No PM10 threshold value has been identified below which there is NO observed damage to health
Importance of anomalous PM10 concentrations even if regulatory daily limit is not exceeded
RST approach to identify anomalous PM10 values
ALICE May 2006
ALICE May 2007
ALICE May 2008
ALICE May 2009
ALICE May 2010
ALICE May 2011
ALICE May 2012

## Slide 39
ALICE
PM10 concentration – May 2008
ALICE PM10 – May 2008
PM10 anomalies under exceedance limit
E.g. Rossellino monitoring station
Over-threshold
(>50mg/m3) PM10 concentrations (due to dust contribution)
Under-threshold
(<50mg/m3) PM10 concentrations (due to dust contribution)
Under-threshold
(<50mg/m3) PM10 concentrations (probably due to anthropogenic contribution)

## Slide 40
The RST application to ground PM10 time-series permits us to identify anomalous PM10 concentrations under exceedance limit. The comparison with RSTDUST products allows to evaluate the source of such under-threshold anomalies (natural or anthropogenic source).
To quantify dust contribution, RSTDUST maps were used instead of forecast maps, as suggested by EC. This permitted us to recognize dust outbreaks with greater reliability
Conclusions
The RSTDUST algorithm guarantees, in comparison with fixed threshold methodologies, improved performances both in terms of reliability (very low rate of false positives) and sensitivity (lower rate of missed identifications);
  Being based only on satellite data at hand, RSTDUST is intrinsically exportable on whatever satellite sensor having VISible and TIR split-window capabilities

## Slide 41: Airborne dust identification from space: a new, MSG/SEVIRI-based method for air quality assessment (valerio.tramutoli@unibas.it) Main References: Marchese, F., F. Sannazzaro, A. Falconieri, C. Filizzola, N. Pergola, and V. Tramutoli (2017), An enhanced satellite-based algorithm for detecting and tracking dust outbreaks by means of SEVIRI data, Remote Sens., 9(6), 1–24, doi:10.3390/rs9060537. Sannazzaro F, Pergola N, Corrado R, Filizzola C, Marchese F, Mazzeo G, Paciello R, Tramutoli V (2014). A New Approach for Detecting and Monitoring Saharan Dusts from Space. Geoinformatics & Geostatistics: An Overview S1. doi:10.4172/2327-4581.S1-019 Sannazzaro F, Filizzola C, Marchese F, Corrado R, Paciello R, Mazzeo G, Pergola N, Tramutoli V, (2013). Identification of dust outbreaks on infrared msg-seviri data by using a Robust Satellite Technique (RST). Acta Astronautica (ISSN:0094-5765). 93, pp. 64- 70.
Thank you